## Slide 1: IAS machine
IAS computer at the Smithsonian National Museum of American History
Weight: 1,000 pounds (450 kg)
First electronic computer to be built at the Institute for Advanced Study (IAS) in Princeton, New Jersey.
von Neumann machine
The computer was built from late 1945 until 1951. It was in operation until July 15, 1958.
It used 1,700 vacuum tubes (triode types: 6J6, 5670, 5687, a few diodes: type 6AL5, 150 pentodes to drive the memory CRTs, and the 40 memory CRTs)

## Slide 2: IAS Architecture
The IAS machine was a binary computer with a 40-bit word, storing two 20-bit instructions in each word.
The memory was 1,024 words (5.1 kilobytes).
Negative numbers were represented in "two's complement" format.
It had two general-purpose registers available: the Accumulator (AC) and Multiplier/Quotient (MQ).

## Slide 3: IAS structure and Memory formats

## Slide 5: How does IAS machine work?

## Slide 6: How does IAS Machine work?
Address (12 bits) | Contents (40 bits)
126H | 03 A52H 01 507H (1st Inst 2nd Inst)
127H | 02 A53H 04 508H (3rd Inst 4th Inst)
128H | 01 A54H 02 509H (5th Inst 6th Inst)
CPU
Control
Unit
ALU
IR
PC
MAR
MBR
Data
Bus
Address
Bus
Control
Bus
Program
in
RAM(40 bits)
IBR

## Slide 7: STEP-1: PC is loaded with RAM address containing 1st & 2nd instructions of program
Address (12 bits) | Contents (40 bits)
126H | 03 A52H 01 507H (1st Inst 2nd Inst)
127H | 02 A53H 04 508H (3rd Inst 4th Inst)
128H | 01 A54H 02 509H (5th Inst 6th Inst)
CPU
Control
Unit
ALU
IR
PC 126H
MAR
MBR
Data
Bus
Address
Bus
Control
Bus
IBR

## Slide 8: STEP-2: MAR is loaded content of PC (with RAM address containing 1st & 2nd instructions of program)
Address (12 bits) | Contents (40 bits)
126H | 03 A52H 01 507H (1st Inst 2nd Inst)
127H | 02 A53H 04 508H (3rd Inst 4th Inst)
128H | 01 A54H 02 509H (5th Inst 6th Inst)
CPU
Control
Unit
ALU
IR
PC 126H
MAR 126H
MBR
Data
Bus
Address
Bus
Control
Bus
IBR

## Slide 9: STEP-3: Address on Address bus, Memory location 126H selected
Address (12 bits) | Contents (40 bits)
126H | 03 A52H 01 507H (1st Inst 2nd Inst)
127H | 02 A53H 04 508H (3rd Inst 4th Inst)
128H | 01 A54H 02 509H (5th Inst 6th Inst)
CPU
Control
Unit
ALU
IR
PC 126H
MAR 126H
MBR
Data
Bus
Address
Bus 126H
Control
Bus
IBR

## Slide 10: STEP-4: Read Machine code of 1st and 2nd Instructions
Address (12 bits) | Contents (40 bits)
126H | 03 A52H 01 507H (1st Inst 2nd Inst)
127H | 02 A53H 04 508H (3rd Inst 4th Inst)
128H | 01 A54H 02 509H (5th Inst 6th Inst)
CPU
Control
Unit
ALU
IR
PC 126H
MAR 126H
MBR 03 A52H 01 507H
(1st Inst 2nd Inst)
Data
Bus
Address
Bus 126H
Control
Bus READ
IBR

## Slide 11: STEP-5: PC is incremented to point next (3rd and 4th ) Instructions to be fetched
Address (12 bits) | Contents (40 bits)
126H | 03 A52H 01 507H (1st Inst 2nd Inst)
127H | 02 A53H 04 508H (3rd Inst 4th Inst)
128H | 01 A54H 02 509H (5th Inst 6th Inst)
CPU
Control
Unit
ALU
IR
PC 127H
MAR
MBR 03 A52H 01 507H
(1st Inst 2nd Inst)
Data
Bus
Address
Bus
Control
Bus
IBR

## Slide 12: STEP-6: OPCODE of 1st Instructions into IR, Address part into MAR, 2nd Instruction into IBR
Address (12 bits) | Contents (40 bits)
126H | 03 A52H 01 507H (1st Inst 2nd Inst)
127H | 02 A53H 04 508H (3rd Inst 4th Inst)
128H | 01 A54H 02 509H (5th Inst 6th Inst)
CPU
Control
Unit
ALU
IR 03H
PC 127H
MAR A52H
MBR 03 A52H 01 507H
(1st Inst 2nd Inst)
Data
Bus
Address
Bus 126H
Control
Bus READ
IBR 01 507H
(2nd Inst)

## Slide 13: STEP-7: 1st Instructions Decoded, Executed
Address (12 bits) | Contents (40 bits)
126H | 03 A52H 01 507H (1st Inst 2nd Inst)
127H | 02 A53H 04 508H (3rd Inst 4th Inst)
128H | 01 A54H 02 509H (5th Inst 6th Inst)
CPU
Control
Unit 03H
ALU
IR 03H
PC 127H
MAR A52H
MBR 03 A52H 01 507H
(1st Inst 2nd Inst)
Data
Bus
Address
Bus A52H
Control
Bus
IBR 01 507H
(2nd Inst)

## Slide 14: STEP-8: 2nd Instructions processing begins: OPCODE into IR, Address into MAR
Address (12 bits) | Contents (40 bits)
126H | 03 A52H 01 507H (1st Inst 2nd Inst)
127H | 02 A53H 04 508H (3rd Inst 4th Inst)
128H | 01 A54H 02 509H (5th Inst 6th Inst)
CPU
Control
Unit
ALU
IR 01H
PC 126H
MAR 507H
MBR 03 A52H 01 507H
(1st Inst 2nd Inst)
Data
Bus
Address
Bus 507H
Control
Bus
IBR 01 507H
(2nd Inst)

## Slide 15: STEP-9: 2nd Instructions Decoded, Executed
Address (12 bits) | Contents (40 bits)
126H | 03 A52H 01 507H (1st Inst 2nd Inst)
127H | 02 A53H 04 508H (3rd Inst 4th Inst)
128H | 01 A54H 02 509H (5th Inst 6th Inst)
CPU
Control
Unit 01H
ALU
IR 01H
PC 127H
MAR 507H
MBR 03 A52H 01 507H
(1st Inst 2nd Inst)
Data
Bus
Address
Bus 507H
Control
Bus
IBR 01 507H
(2nd Inst)

## Slide 16: STEPS: 2- 9 are repeated
Address (12 bits) | Contents (40 bits)
126H | 03 A52H 01 507H (1st Inst 2nd Inst)
127H | 02 A53H 04 508H (3rd Inst 4th Inst)
128H | 01 A54H 02 509H (5th Inst 6th Inst)
CPU
Control
Unit
ALU
IR
PC 127H
MAR 127H
MBR
Data
Bus
Address
Bus
Control
Bus
IBR

## Slide 18: IAS Architecture
It was an asynchronous machine, meaning that there was no central clock regulating the timing of the instructions.
One instruction started executing when the previous one finished.
The addition time was 62 microseconds
The multiplication time was 713 microseconds.

## Slide 19: Operations of ISA are of three types
Moves between the accumulator, multiplier quotient register, and memory
ALU operations such as add, subtract, multiply, and divide
Unconditional and conditional branch instructions that redirect program flow
The von Neumann ISA consists of 21 instructions

## Slide 20
Address | Contents
08A | 010FA 210FB
08B | 010FA 0F08D
08C | 020FA 210FB